## Slide 1
RRAM Device Modelling Using COMSOL Multiphysics and MATLAB LiveLink
Presented by: Sweta Maurya | Scholar ID: 2315080
B.Tech., 7th Semester
Under the guidance of Dr. Shivendra Kumar Pandey
Department of Electronics and Instrumentation Engineering
National Institute of Technology Silchar • June–July 2026
SN Bose Internship Program, 2026

## Slide 2
1. Motivation & Problem Context
Why filamentary RRAM needs coupled device modelling
02
SN Bose Internship Program 2026 • RRAM Device Modelling
RRAM switching
Resistance changes between a high-resistance state (HRS) and low-resistance state (LRS) through formation and rupture of a conductive filament.
Why physics matters
Switching is coupled to Joule heating, filament growth/rupture, electrostatics and material properties.
Internship focus
Develop and debug a numerical COMSOL model driven and post-processed through MATLAB LiveLink.
• Study the thermodynamic and electro-thermal framework reported for filamentary RRAM.
• Automate the OFF → SET → ON → RESET sequence and extract device-level quantities.
• Build a reproducible workflow that can later support quantitative validation against literature.

## Slide 3
1. RRAM Structure & Switching Mechanism
From oxygen vacancies to conductive-filament switching
03
SN Bose Internship Program 2026 • RRAM Device Modelling
RRAM states
• HRS: filament is interrupted • LRS: conductive filament forms
SET / RESET
SET → filament grows → LRS RESET → filament ruptures → HRS
Physical picture
Applied electric field drives oxygen-ion / vacancy redistribution, changing the conductive path.
KEY IDEA: FILAMENT FORMATION & RUPTURE

## Slide 4
3. Theoretical Framework
Niroula–Karpov thermodynamic modelling
04
SN Bose Internship Program 2026 • RRAM Device Modelling
FREE-ENERGY MODEL
• For a given applied bias, the model evaluates the total free energy as a function of filament radius.
• The equilibrium filament radius is obtained by minimizing the total free energy.
• The approach is repeated across voltage/current sweeps to construct switching behaviour.
Chemical / volume
Phase-change contribution
Surface
Interface energy + surface tension
Electrostatic
Electric-field energy in the dielectric/gap
Thermal
Joule-heating-related heat energy
Applied bias
→
Electro-thermal fields
→
Free-energy vs. radius
→
Minimum-energy state

## Slide 5
4. COMSOL Device Model
2D axisymmetric geometry, materials and multiphysics
05
SN Bose Internship Program 2026 • RRAM Device Modelling
• 2D axisymmetric model constructed in COMSOL Multiphysics 6.0.
• Device stack includes TiN electrodes, HfO₂ dielectric, Hf layer, HfO₂−x filament and an insulating gap.
• The geometry was parameterized so filament radius and gap length could be varied during the switching calculations.
MODEL DOMAINS
Top TiN
→
HfO₂ / Hf
→
Filament + gap
→
Bottom TiN

## Slide 6
5. Multiphysics Setup
Coupling heat, electric current and circuit physics
06
SN Bose Internship Program 2026 • RRAM Device Modelling
Heat Transfer in Solids
Solves device temperature using heat conduction and Joule-heating input.
Electric Currents
Computes electric potential and current density in conductive domains.
Electrical Circuit
Represents the external drive circuit and voltage/current source behaviour.
Electromagnetic Heating
Feeds Joule heating from the electrical model into the thermal model.
• A free triangular mesh was used, with finer element density near the filament–electrode interface.
• The report also defines surface-to-ambient radiation on exposed surfaces.

## Slide 7
6. MATLAB–COMSOL LiveLink Workflow
From parameter sweeps to automated switching-cycle data
07
SN Bose Internship Program 2026 • RRAM Device Modelling
MATLAB parameters
→
COMSOL model build
→
Solve multiphysics
→
Extract fields
→
Free-energy minimization
→
Store MAT data
• Four COMSOL model states were organized as RRAM_OFF, RRAM_ON, RRAM_SET and RRAM_RESET.
• MATLAB LiveLink was used to rebuild/run models, override parameters, extract quantities and aggregate results.
• The workflow was designed to execute a complete switching cycle rather than isolated manual simulations.
POST-PROCESSING
• Saved .mat tables preserve stage-wise data for later I–V plotting and analysis.

## Slide 8
6. MATLAB–COMSOL LiveLink Workflow
How MATLAB controls the COMSOL simulation
08
SN Bose Internship Program 2026 • RRAM Device Modelling
1. MATLAB
Sets parameters such as voltage, material values and switching conditions.
2. COMSOL
Builds and solves the coupled electrical + thermal device model.
3. MATLAB
Reads current, temperature, filament radius and free-energy data for analysis.
→
→
AUTOMATION LOOP
• The process is repeated for the OFF, SET, ON and RESET stages.
• This reduces manual parameter changes and result collection in COMSOL.
• The extracted data are saved in MATLAB for plotting and analysis.
Why LiveLink is useful
It connects MATLAB scripting with the COMSOL solver, making repeated simulations, parameter changes and result extraction easier to automate.
MATLAB = CONTROL & ANALYSIS | COMSOL = PHYSICS SOLVER

## Slide 9
8. Simulation Status & Generated Data
What was successfully achieved
09
SN Bose Internship Program 2026 • RRAM Device Modelling
Pipeline status
All four COMSOL modules build and solve successfully inside MATLAB–COMSOL LiveLink after debugging.
Automated cycle
The driver runs OFF → SET → ON → RESET, including free-energy minimization and data aggregation.
Output data
Stage-wise tables capture voltage, current, temperature, filament/gap parameters and free-energy terms.

## Slide 10
9. Data Processing & I–V Characterization
Separate simulation from plotting for reproducible analysis
10
SN Bose Internship Program 2026 • RRAM Device Modelling
• A dedicated MATLAB post-processing script, plot_RRAM_IV.m, loads saved .mat data.
• Three complementary views were implemented: combined I–V, stage-wise I–V, and logarithmic-scale I–V.
• The plotted data currently reveal numerical/model issues that must be resolved before physical validation.
IMPORTANT OBSERVATION
• The report identifies an anomalous device-voltage scale and a non-convergent RESET free-energy minimization in the examined run.

## Slide 11
9. Preliminary Results & Current Status
What the present simulation workflow produces
11
SN Bose Internship Program 2026 • RRAM Device Modelling
EXAMPLE COMSOL TEMPERATURE OUTPUT
What is working
The COMSOL models run through the MATLAB–LiveLink workflow and return stage-wise simulation data.
What the temperature plot shows
The device develops a non-uniform temperature distribution, demonstrating the electro-thermal part of the model.
What still needs improvement
RESET minimization and the extracted device-voltage scale require further investigation before quantitative I–V validation.

## Slide 12
11. Limitations & Current Scope
What the internship did—and did not—establish
12
SN Bose Internship Program 2026 • RRAM Device Modelling
Established during internship
A working, automated COMSOL–MATLAB modelling infrastructure; systematic debugging; data extraction and I–V post-processing.
Not yet established
Physically validated switching curves, ramp-rate dependence, cycle-to-cycle variation and quantitative agreement with literature.
• RESET free-energy minimization remains non-convergent in the examined run.
• Device-voltage scaling is anomalous and requires investigation of the COMSOL circuit configuration.
• The report explicitly treats the model as a working, debugged simulation infrastructure rather than a completed validated device model.
NO EXPERIMENTAL FABRICATION
The internship work was computational; no experimental device fabrication was performed.

## Slide 13
12. Technical Learning Outcomes
Skills developed through the internship
13
SN Bose Internship Program 2026 • RRAM Device Modelling
Multiphysics FEM
Translated physical RRAM geometry into coupled Heat Transfer, Electric Currents and Electrical Circuit models.
MATLAB LiveLink
Programmatic control of COMSOL: model building, parameter sweeps, solving and result extraction.
Systematic debugging
Learned to isolate errors across MATLAB syntax, COMSOL parameters, selections, mesh, tables and server state.
Simulation architecture
Separated model-building, simulation, data aggregation and plotting into reusable stages.
• Most importantly: intermediate quantities and stage-wise data should be inspected before trusting a final I–V result.

## Slide 14
13. Future Scope & Conclusion
Path from a functional pipeline to validated RRAM characteristics
14
SN Bose Internship Program 2026 • RRAM Device Modelling
NEXT STEPS
• Resolve RESET free-energy convergence and identify the stable gap-length solution.
• Resolve the device-voltage scaling / circuit-terminal configuration issue.
• Generate and validate the baseline I–V curve after the above fixes.
• Run ramp-rate and cycle-to-cycle studies and compare against reference literature.
• Quantitatively benchmark SET/RESET ON/OFF states, current ratios and switching behaviour.
CONCLUSION
• The internship established a COMSOL–MATLAB framework for numerical RRAM modelling.
• The main practical contribution was making the inherited simulation pipeline executable and systematically debugging it.
• The work provides a foundation for completing physical validation in the next stage.
Takeaway
A reliable simulation workflow is the prerequisite for trustworthy device-level conclusions.

## Slide 15
Thank You
Sweta Maurya • Scholar ID 2315080
Selected references
• D. Niroula & V. G. Karpov, “Comprehensive numerical modeling of filamentary RRAM devices…” (2018). • COMSOL Multiphysics 6.0 documentation and COMSOL LiveLink for MATLAB documentation. • RRAM literature cited throughout the internship report on HfO₂ switching and filamentary behaviour.
SN Bose Internship Program 2026 • National Institute of Technology Silchar